## Slide 1: CubeSat Team

## Slide 2: Conceptual View
Order of Operations:
Detector receives a gamma event
Flight Computer adds Time, GPS, and Attitude stamps.
Packets are formed and stored
Data is transmitted to Ground
Network

## Slide 3: Requirements
  The CubeSat shall determine and relay a relative position solution (i.e., relative to the formation) with an accuracy of 10 meters (1 standard deviation)
  The CubeSat shall determine and relay a relative attitude solution with an accuracy of 10 mRad.
  The CubeSat shall maintain a clock offset or timing accuracy (relative to the formation) better than 10 µs.

## Slide 4: Requirements – Derived
Shall accept X-ray Detector as a payload
  Supplies payload with power (5W) and communication requirements
  Provides environmental data (time, attitude, position) to payload with priority
  Receives data from payload to transmit to ground network
Shall meet NASA CubeSat Launch Initiative requirements
  Structural, electrical, and other requirements are listed at
    http://www.nasa.gov/pdf/627972main_LSP-REQ-317_01A.pdf
Shall have the following subsystems
  Structure
  Attitude Determination and Navigation Control Systems
  Communication
  Power Management

## Slide 5: Navigation Systems

## Slide 6: Position Determination
Requirement
  The CubeSat shall determine and relay a position solution with an accuracy of 10 meters (1 standard deviation)
Solution
  Global Positioning Systems

## Slide 7: GPS in Space
GPS satellites are in Middle Earth Orbit
CubeSat operates in Low Earth Orbit
Two hardware components
  GPS Receiver
  GPS Antenna
    Patch Antenna
    Boxed Antenna

## Slide 8: GPS Receiver
Name | piNAV-L1 GPS, Skyfoxlabs | OEM615, Novatel | CPS12-V1, SpaceQuest
Size(mm) | 71 by 35 by 12.5 | 71 by 46 by 11 | 100 by 70 by 25
Power (W) | .540 | 1 | 1.2
Weight (g) | 47 | 24 | 160
Space Heritage | Projected, December 2016 | Unlisted; flown by Colorado CubeSat team | SpaceX, NASA, and USAF
Notes: Cost is 8K 12K(around owned however) and 29K respectively

## Slide 9: GPS Antenna
Name | Single Frequency Microstrip, Antdevco | ANT-GPS, SpaceQuest | 2G15A-XTB-1-N, AntCom
Type | Patch | Patch | Boxed
Size(in) | 3 x 3 | 2 x 2 | 2.6 Dia
Weight(g) | 100 | 82 | 110
Space Heritage | DOD, NASA, and USAF | SpaceX, NASA, and USAF | HASP
Notes: 5K and 3K respectively

## Slide 10: Attitude Determination

## Slide 11: Attitude Determination
Requirements
  Shall be accurate to within 10 mRad (0.57º)
  Shall not interfere electronically or magnetically with payload
  Shall not be magnetically-based
  All components are preferred to have space heritage

## Slide 12: Attitude Determination
Sun Sensors
  Produces a vector to the sun based on 2-axis analog output from photovoltaic cells

## Slide 13: Sun Sensors
Name | P110 Gomspace | SSoC-A60, SOLARMEMS | Cubesat Sun Sensor, SSBV | MSS-01 Sun Sensor, Space Micro
Size(mm) | 5.5 x 11 x 11 | 50 x 12 x 30 | 33 x 11 x 6 | 35 x 25 x 25
Power (W) | N/A | 0.036 | 0.050 | N/A
Accuracy (degrees) | N/A | 0.3 | 0.5 | 1
Weight (g) | N/A | 25 | 5 | 36
Space Heritage | AAU-Cubesat | NANOSAT 1B | UKube‐1 and TDS‐1 | N/A

## Slide 14: Attitude Control

## Slide 15: Attitude Control
Passive Attitude Control
  Using a bar magnet to align with the Earth’s magnetic field
  Will ensure the bottom of the CUBESAT will point nadir

## Slide 16: Communication

## Slide 17: Communication
Requirements
  Industrial Grade Radio
    Withstand the environment
    Reliability and high efficiency
  Data Storage and Transmission
    Store and transfer data packets when link is available
  Desired Orbit for Data Transfer
    Need unit to fly near data stations for downlink

## Slide 18: Working Assumptions
Assume one event per orbit
Assume communication available to 3 base stations across the United States (Honolulu, Boulder, Fairbanks, maybe Crookston)
Assume circular LEO
Assume each data set on the order of 10 MiB

## Slide 19: Questions/Solutions
How much power is required for the broadcast signal?
  Link budget
How much time will be available during each orbit for communication?
  Link budget
  Orbital parameters
Is it possible to transmit all data in the time allotted?
  Link budget

## Slide 20: Communication – Scenario 1
GPS
-Attitude
-Position
-Time
Power
-Wattage
-Battery
Radio
Antenna
Flight Computer
-Assemble packet
Gamma Ray Detector
Used if data packets are large and connecting to ground stations is difficult

## Slide 21: Communication – Scenario 2
GPS
-Attitude
-Position
-Time
Power
-Wattage
-Battery
FunCube
Antenna
Flight Computer
-Assemble packet
Gamma Ray Detector
Cheaper approach if data packets are small enough

## Slide 22: Power Management

## Slide 23: Power Management
Requirements
  Supply Subsystems with Power Demands
    Shall supply power demands for payload and subsystems for full orbital period.
    Shall supply adequate battery storage to supply priority systems through non-sun lit portions of orbit.
  Power Management System
    Shall have Power Safety Mode, provides priority systems shut off sequence to conserve low batteries.
    CubeSat shall be able to launch with all systems powered off and batteries fully discharged. Shall be able to power-on systems once deployed.
    Shall supply ease of access to power system’s inputs and terminals.

## Slide 24: Power Management
 | Communications Systems | ADNCS | Power Systems | Payload
Scenario One | Radio: 1W | GPS: 1W |  | 5 W
Scenario Two (preferred) | Radio: <1W | GPS: 1.2W |  | 5 W
Notes: The “Best” scenario for the Radio is if we can somehow use the Funcube dongle.

## Slide 25: Power Management
Consumption
  All electrical hardware components
  Power Management Board
Supply
  Photovoltaic cells convert sunlight to power
  Power management board distributes power to hardware and batteries
Subsystems

## Slide 26: Power Management
Solar Panels  Qty of 4 required
  Suppliers include ClydeSpace and GOMSpace
Integrated Sun sensors
  Reduce power overhead
  Alleviate space constraints
Batteries
  Charge while on “Sun-side” of orbit
  Power CubeSat through dark side
Power management board
  Distributes power
  Read and controls hardware in and output usage
GOMSpace 4 per 3U panel
  Total Power Produced Per Panel ~6.81 W
ClydeSpace 3U Solar Panel(s)
  Total Power Produced Per Panel ~6.26 W
GOMSpace
ClydeSpace