## Slide 1: Power Systems and Management
Supply Subsystems with Power Demands
  Must supply power demands for payload and subsystems for full orbital period.
  Must supply adequate battery storage to supply priority systems through non-sun lit portions of orbit.
Power Management System
  Must have Power Safety Mode, provides priority systems shut off sequence to conserve low batteries.
  CubeSat must be able to launch with all systems powered off and batteries fully discharged. Must be able to power on systems once deployed.
  Must supply ease of access to power system’s inputs and terminals.
Requirements

## Slide 2: Sub-System’s Power Demands
 | Communications | ADNCS | Flight Computer/Payload(HASP) | Total Wattage Demand
Worst Scenario | Radio: 2W | GPS: 540mW |  | 
Better Scenario | Radio: 1W | GPS: 1W |  | 
Best Scenario | Radio: <1W | GPS: 1.2W |  | 
Final Comments
Notes: The “Best” scenario for the Radio is if we can somehow use the Funcube dongle.

## Slide 3: Solutions to Desired Power Consumption:
Cover four side faces with solar panels which include sun/horizon sensors
Batteries *ADD MORE INFO
Power Management Board
Subsystems

## Slide 4: Option One:
3U Solar panel(s) Qty of 4 desired
  From ClydeSpace/GOMSpace
Can purchase pre-mounted Sun/Horizon Sensors for attitude determination
Unit Price ~ $6,700 (ClydeSpace)
  Total ~ $26,000 (4 units)
Unit Price ~ $3,100 (GOMSpace)
  Total ~ $36,800 (12 1U units)
GOMSpace 4 per 3U panel
  Total Power Produced Per Panel ~6.81 W
ClydeSpace 3U Solar Panel(s)
  Total Power Produced Per Panel ~6.26 W
* Rule of thumb; true power ~ 60% of total power produced.
GOMSpace
ClydeSpace