## Slide 2: Position Determination
Requirement:
  Must be able to determine Position within an Accuracy of 10 meters
Solution:
  Global Positioning Satellites (GPS)

## Slide 3: GPS in Space
GPS satellites are in Middle earth orbit
We will be in Low earth Orbit
Comprised of two pieces
  GPS Receiver
  GPS Antenna
    Patch Antenna
    Boxed Antenna

## Slide 4: GPS Receiver
Name | piNAV-L1 GPS made by Skyfoxlabs | OEM615 made by novatel | CPS12-V1
Size(mm) | 71 by 35 by 12.5 | 71 by 46 by 11 | 100 by 70 by 25
Power | 540mW | 1 W | 1.2 W
Weight (g) | 47 | 24 | 160g
Space Heritage | First Flight on December 2016 | Unlisted but used on HASP | Past Customers include SpaceX, NASA, and USAF
Notes: Cost is 8K 12K and 29K respectively

## Slide 5: GPS Antenna
Name | Single Frequency Microstrip Patch Antenna by Antdevco | ANT-GPS by SpaceQuest | 2G15A-XTB-1-N by AntCom
Type | Patch | Patch | Boxed
Size | 3 in by 3 in | 2 in by 2in | 2.6in Diameter by .69 in
Weight | 100g | 82g | 110g
Space Heritage | Past Customers include DOD, NASA, and USAF | Past Customers include SpaceX, NASA, and USAF | Used on HAPS
Notes: 5K and 3K respectively