## Slide 1: CubeSat Team
Ethan Arendt Brian Hanson Justin Seifert
Charles Denis Nicholas Janak Ben Setterholm
Jacob Gustafson Tim Kukowski Nicholas SloaN

## Slide 2: System Architecture
  Team Lead/Structure
  Charles Denis
ADNCS
Jacob Gustafson
Brian Hanson
Nicholas Sloan
Communications
Ben Setterholm
Tim Kukowski
Power Management
Ethan Arendt
Justin Seifert
Nicholas Janak

## Slide 3: Background
  Payload
    Gamma Ray Detector (GRD)
  What it does?
    Detect Gamma Ray Events in order to conceptually prove deep space navigation concepts.

## Slide 4: Conceptual View
Order of Operations:
CubeSat polls environment
GRD receives a gamma event
Flight Computer adds Time, GPS, and Attitude stamps.
Data Packets formed and stored
Data is transmitted to Ground
Network

## Slide 5: Requirements
  The CubeSat shall determine and relay a relative position solution (i.e., relative to the formation) with an accuracy of 10 meters (1 standard deviation)
  The CubeSat shall determine and relay a relative attitude solution with an accuracy of 10 mRad.
  The CubeSat shall maintain a clock offset or timing accuracy (relative to the formation) better than 10 µs.

## Slide 6: Requirements – Derived
Shall accept X-ray Detector as a payload
  Supplies payload with power (5W) and communication requirements
  Provides environmental data (time, attitude, position) to payload with priority
  Receives data from payload to transmit to ground network
Shall meet NASA CubeSat Launch Initiative requirements
  Structural, electrical, and other requirements are listed at
    http://www.nasa.gov/pdf/627972main_LSP-REQ-317_01A.pdf
Shall meet “Industrial Grade” environmental requirements
  Defined by ________________ as -40ºC to 85ºC

## Slide 7: Block Diagram

## Slide 8: Navigation

## Slide 9: Navigation - GPS
Requirement
  The CubeSat shall determine and relay a position solution with an accuracy of 10 meters (1 standard deviation)
Solution
  Global Positioning Systems

## Slide 10: Navigation - GPS
GPS satellites are in Middle Earth Orbit
CubeSat operates in Low Earth Orbit
Two hardware components
  GPS Receiver
  GPS Antenna
    Patch Antenna
    Boxed Antenna

## Slide 11: Navigation – GPS Receiver
Specifications | piNAV-L1 GPS, Skyfoxlabs | OEM615, Novatel | CPS12-V1, SpaceQuest
Size(mm) | 71 x 35 x 12.5 | 71 x 46 x 11 | 100 x 70 x 25
Power (W) | .540 | 1 | 1.2
Weight (g) | 47 | 24 | 160
Space Heritage | Projected, December 2016 | Unlisted; flown by Colorado CubeSat team | SpaceX, NASA, and USAF
Cost($) | 8,000 | 6,000* | 29,000
*Currently owned and wouldn’t contribute to total budget
Notes: Cost is 8K 12K(around owned however) and 29K respectively

## Slide 12: Navigation – GPS Antenna
Specifications | Single Frequency Microstrip, Antdevco | ANT-GPS, SpaceQuest | 2G15A-XTB-1-N, AntCom
Type | Patch | Patch | Boxed
Size(in) | 3 x 3 | 2 x 2 | 2.6 Dia
Weight(g) | 100 | 82 | 110
Space Heritage | DOD, NASA, and USAF | SpaceX, NASA, and USAF | HASP
Cost ($) | 5,000 | 3,000 | 1,000*
*Currently owned and wouldn’t contribute to total budget
Notes: 5K and 3K respectively

## Slide 13: Attitude Determination

## Slide 14: Attitude Determination
Requirements
  Shall be accurate to within 10 mRad (0.57º)
  Shall not interfere electronically or magnetically with payload
  All components are preferred to have space heritage

## Slide 15: Attitude Determination
Specifications | P110 Gomspace | SSoC-A60, SOLARMEMS | Cubesat Sun Sensor, SSBV | MSS-01 Sun Sensor, Space Micro
Size(mm) | 5.5 x 11 x 11 | 50 x 12 x 30 | 33 x 11 x 6 | 35 x 25 x 25
Power (W) | N/A | 0.036 | 0.050 | N/A
Accuracy (mRad) | N/A | 10.5 | 17.5 | 35.0
Weight (g) | N/A | 25 | 5 | 36
Space Heritage | AAU-Cubesat | NANOSAT 1B | UKube‐1 and TDS‐1 | N/A
Cost ($) | Included in solar panels | 3362.35 | 3300 | N/A
Sun Sensors
  Produces a vector to the sun based on 2-axis analog output from photovoltaic cells
Hardware

## Slide 16: Attitude Control

## Slide 17: Attitude Control
Passive Attitude Control
  Using a bar magnet to align with the Earth’s magnetic field
  Will ensure the bottom of the CUBESAT will point nadir

## Slide 18: Communication

## Slide 19: Communication - Orbit
3 – 4 ground based communication stations available across United States
  Anchorage, Boulder, Honolulu, Crookston
Orbit shall coincide with as many ground stations as possible
  1.5 hour orbital period in LEO
  5 minute communication window per station
  Target: 3 stations
Orbital parameters shall not interfere with other spacecraft

## Slide 20: Communication - Data
One event per orbit assumed (<10 MB of data per event)
Key requirements
  Downlink signal shall have enough power to be received at ground stations
  Data must be stored between communication windows
  Downlink speed shall be fast enough to send all stored information per communication window (100 kbps minimum)
  Shall provide minimal uplink capability for error checking and basic commands
Link Budget

## Slide 21: Communication - Hardware
Requirements
  Industrial Grade Radio
    Withstand the environment
    Reliability and high efficiency

## Slide 22: Communication - Hardware
Specifications | FunCube Dongle Pro+ | MM2-TTL, Freewave | CubeSat TX Patch Antenna
Size (in) | 3 x 0.75 x 0.15 | 2 x 1.4 x 0.38 | 3 Dia
Power (W) | N/A | 0.10 to 1.0 | < 6
Weight (g) |  | 14 | 50
Data Transfer Rate (kbps) | N/A | 115.2 | N/A
Space Heritage | FunCube Satellites |  | Ukube-1 (Clyde Sapce)
Cost ($) | 325 | 650 | 4,750

## Slide 23: Power Management

## Slide 24: Power Management
Requirements
  Supply Subsystems with Power Demands
    Shall supply power demands for payload and subsystems for full orbital period.
    Shall supply adequate battery storage to supply priority systems through non-sun lit portions of orbit.
  Power Management System
    Shall have Power Safety Mode, provides priority systems shut off sequence to conserve low batteries.
    CubeSat shall be able to launch with all systems powered off and batteries fully discharged. Shall be able to power-on systems once deployed.
    Shall supply ease of access to power system’s inputs and terminals.

## Slide 25: Power Management
Specifications | OBC | Com Systems | ADNCS | Power Systems | Payload
Scenario One | 500mW | Radio: 1W | GPS: 1W SOLARMEMS SSoC-A60: 36mW | Power Management Board: Variable Solar Cells: ~2.4mW | 5 W
Scenario Two (preferred) | 500mW | Radio: <1W | GPS: 1.2W SSBV sun sensor: 50mW | Power Management Board: Variable Solar Cells: ~2.4mW | 5 W
Notes: The “Best” scenario for the Radio is if we can somehow use the Funcube dongle.

## Slide 26: Power Management
Consumption
  All electrical hardware components
  Power Management Board
  Solar Cells (for conversion)
Supply
  Photovoltaic cells convert sunlight to power
  Power management board distributes power to hardware and batteries
Subsystems

## Slide 27: Power Management
Solar Panels  Qty of 4 required
  Suppliers include ClydeSpace and GOMSpace
Integrated Sun sensors
  Reduce power overhead
  Alleviate space constraints
Batteries
  Charge while on “Sun-side” of orbit
  Power CubeSat through dark side
Power management board
  Distributes power
  Read and controls hardware in and output usage
GOMSpace 4 per 3U panel
  Total Power Produced Per Panel ~6.81 W
ClydeSpace 3U Solar Panel(s)
  Total Power Produced Per Panel ~6.26 W
GOMSpace
ClydeSpace

## Slide 28: Deliverables at CDR