## Slide 1: CubeSat
Critical Design Review

## Slide 2: Agenda
    Introduction
    Motivation
    Approach
    Budget
    Design
    Standards
    FMEA
    Conclusion
Charlie

## Slide 3: Introduction
Charlie
  Team Lead/Structure
  Charles Denis
ADNCS
Jacob Gustafson
Brian Hanson
Nicholas Sloan
Communications
Ben Setterholm
Tim Kukowski
Power Management
Ethan Arendt
Justin Seifert
Nicholas Janak

## Slide 4: Motivation
Charlie

## Slide 5: Motivation
Payload
  Gamma Ray Intensity Detector (GRID)
What GRID does?
  Detect Gamma Ray Events to conceptually prove deep space navigation concepts
Charlie
Figure 1. This figures shows six examples of known Gamma Ray bursts from our universe. The data in the plots represents the relation between Kilo-Electron Volts and Seconds in time.

## Slide 6: Motivation
Payload
  Gamma Ray Intensity Detector (GRID)
What GRID does?
  Detect Gamma Ray Events to conceptually prove deep space navigation concepts
Charlie
Figure 1. This figures shows six examples of known Gamma Ray bursts from our universe. The data in the plots represents the relation between Kilo-Electron Volts and Seconds in time.

## Slide 7: Motivation
Requirements
  The CubeSat shall determine and relay a relative position solution (i.e., relative to the formation) with an accuracy of 10 meters (1 standard deviation)
  The CubeSat shall determine and relay a relative attitude solution with an accuracy of 10 mRad.
  The CubeSat shall maintain a clock offset or timing accuracy (relative to the formation) better than 10 µs.
Charlie

## Slide 8: Motivation
Derived Requirements
  Shall accept “GRID” as a payload
    Supplies payload with power (3~5W/hr) and communication requirements
    Provides environmental data (time, attitude, position) to payload with priority
    Receives data from payload to transmit to ground network
  Shall meet NASA CubeSat Launch Initiative requirements
    Structural, electrical, and other requirements are listed at
      http://www.nasa.gov/pdf/627972main_LSP-REQ-317_01A.pdf
Charlie

## Slide 9: Design - Model
Solidworks Model HERE

## Slide 10: Design - Structure
Century College to Manufacture to Specifications
  Sub Contracted by UMN
Charlie

## Slide 11: Design

## Slide 12: Wiring
TO BE COMPLETED

## Slide 13: Design - ADNCS

## Slide 14: DESIGN ADNCS
Passive attitude control decision
TO BE COMPLETED

## Slide 15: Design - Communications

## Slide 16: Design - Com. Equipment
FreeWave Radio @ 915MHz
Whip Antenna
TO BE COMPLETED

## Slide 17: Design - Communications
Ben
Step 1: Active Pinging
Check if any other ground stations are currently in contact with CubeSat
If not, send hail signal once every 3 seconds

## Slide 18: Design - Communications
Ben
Step 2: Establish Connection
CubeSat replies to hail
CubeSat transmits GPS location, heading, and velocity information
CubeSat transmits number of files ready for downlink

## Slide 19: Design - Communications
Ben
Step 3: Computation
Ground station determines communication time

## Slide 20: Design - Communications
Ben
Step 3: Computation
Ground station determines communication time
2°
2000 km

## Slide 21: Design - Communications
Ben
Step 3: Computation
Ground station determines communication time
CubeSat makes contact
Determine range

## Slide 22: Design - Communications
Ben
Step 3: Computation
Ground station determines communication time
CubeSat makes contact
Determine range
Forward time step
  5 second intervals

## Slide 23: Design - Communications
Ben
Step 4: Command
Ground Station sends command code
  transfer queued file
  transfer log file
  diagnostics
  delete queued file
  delete all data files
  delete log file
  reboot OS
  goodbye

## Slide 24: Design - Communications
Ben
Step 5: Transmit Data
point

## Slide 25: Design - Communications
Ben
Step 6: Checksum
point

## Slide 26: Design - Communications
Ben
Step 7: Confirmation
CubeSat checks checksum
CubeSat relays success/failure to ground station
CubeSat marks file for deletion

## Slide 27: Design - Power

## Slide 28: Design – Power Budget
TO BE COMPLETED

## Slide 29: Budget
Attitude Control
Attitude Determination
Navigation
Communication
Power
Manpower
  FREE!

## Slide 30: FMEA
TO BE COMPLETED
Charlie

## Slide 31: Conclusion
Delivered:
TO BE COMPLETED

## Slide 32: Individual Reports

## Slide 33: Design – Data Link Budget
TO BE COMPLETED
Ben